MSS-CASCADE User Manual
# Features
- Completely integrated Modular Signal System “Cascade” type module
- Compliant with the MSS v2.0.0 specification
- Easy installation with connectors and terminal blocks
- Dual extremely sensitive (12-15k ohms) isolated DCC block detectors
- Simple sensitivity adjustment
- Isolated detection to prevent coupling track power and signal systems
- Integrated “foolproof” ISE CKT-IRSENSE optical detector
- Capable of driving a wide variety of signal heads:
  - 3 LED common anode (+)
  - 3 LED common cathode (-)
  - Red/green single LED, 3 wire common anode (+)
  - Red/green single LED, 3 wire common cathode (-)
  - Red/green single LED, 2 wire
- Supports single or dual headed signals for each direction
- Supports MSS “diverging approach indication”
- Configurable signal aspects and approach lighting
- Auxiliary occupancy input for both A and B blocks
# Overview
The MSS-CASCADE module is designed to be compatible with the Modular Signal System v2.0.0 specification ( http://modularsignalsystem.info/ ). It is designed to provide basic ABS signaling functionality at a block boundary. It contains dual integrated DCC current block detectors, an optical detector based on the foolproof Iowa Scaled Engineering CKT-IRSENSE, MSS occupancy bus logic, LED signal drivers, and power supply, which provides the complete “cascade” unit described in the standard.
# Installation
The MSS-CASCADE module is designed to be easy to install.
Track power must be isolated on both rails at each end of the module, per the MSS standard. The connection between one track rail (on the section to be detected) and the modular track power bus must make one pass through the detector's current transformer (T1, the large black tombstone looking item on the PCB). Only one pass is necessary – multiple loops will likely make the detector too sensitive.
Any track elements on the module that you do not want to have detect – such as industry spurs, secondary tracks, etc. - must be isolated from the detected mainline and fed with wires that do not go through the detector transformer.
The MSS-CROSSOVER also requires power to operate. At a minimum, the module needs 8VDC applied to J3, the two position terminal block on the left side of the board. It can accept up to 20 volts AC or DC, so that it can be fed from the Free-mo accessory bus or any other low voltage power supply that might be handy (including DCC track power, if necessary, though it is not recommended).
Once installed, the block detector has to be calibrated to the installed track and wiring. See the “Sensitivity Adjust” section for this simple procedure.
# Sensitivity Adjustment
Contrary to popular belief, an empty track block does not always draw zero current. Because of resistive leakage through scenery (including wooden ties in varying humidity) and capacitive effects between the rails and feeder wires, there's often a very small leakage current. Thus, a sensitivity adjustment is provided to allow you to calibrate this out, minimizing false detection while keeping the very highest levels of sensitivity.
Once the board is installed, apply DCC power to the track bus inputs with absolutely nothing on the track. If the “OCC” red LED comes on solid, turn the sensitivity adjustment potentiometer counter-clockwise with a small flathead screwdriver slowly until the light turns off.
If the “OCC” red LED is off, turn the potentiometer slowly clockwise until the light comes on, then back it off until the light turns off.
Test the sensitivity by placing a locomotive or a piece of resistor-equipped rolling stock across the rails. The OCC light should come on when the equipment is on the track, and turn off after a short delay when the equipment is removed.
If the detector trips without equipment, continue making slight counter-clockwise adjustments until the module no longer detects phantom equipment. Sometimes humidity, changes in track voltage, twisting of wires, etc. can change the amount of quiescent current being drawn and trigger the detector. The detector is adequately sensitive that it can be desensitized quite a bit before it's unable to detect resistor-equipped cars.
# Auxiliary Input
Most signal systems require that any turnout off the signaled mainline must be wired to trigger detection if it's thrown against the main. The aux input pins can be used to connect auxillary contacts on switch machines, ground throws, or more complex items like the Iowa Scaled CKT-TIMELOCK switch time lock simulator into the occupancy bus without a direct electrical interconnection.
When the pins are shorted but no occupancy is detected, the “OCC” red LED will blink and occupancy sent on the MSS bus. If occupancy is detected, the “OCC” red LED will go on solid, regardless of the axillary input.

While it's safest to not connect the auxiliary input terminals to anything but each other through an isolated electrical switch, it is possible to drive them with a logic circuit. If you do want to connect them to some sort of logic, the input is negative true (meaning, 0V triggers occupancy), and never exceed 5VDC or the module will be destroyed.

# Quick Start Guide
1. Set all switches to the “off” position
2. Determine the type of LEDs in your signals and set SW1, switches 1-3 appropriately according to table X-1.

# Configuration Switches

Switch / Bank	Switch	Function
SW1	1	Signal Head Type Configuration / See table X-1
SW1	2
SW1	3
SW1	4	On = Signal A has two signal heads Off = Signal A has a single signal head
SW1	5	On = Signal B has two signal heads Off = Signal B has a single signal head
SW2	1	Signal A Aspect Configuration / See table X-2 if signal A is configured as single headed (SW1-4 = Off) / See table X-3 if signal A is configured as dual headed (SW1-4 = On)
SW2	2
SW3	3	Signal B Aspect Configuration / See table X-2 if signal B is configured as single headed (SW1-5 = Off) / See table X-3 if signal B is configured as dual headed (SW1-5 = On)
SW2	4
SW2	5	On = Signals approach lit Off = Signals always lit

Table X-1: Signal Head Type Configuration

SW1-3	SW1-2	SW1-1	Signal Type
Off	Off	Off	3-wire R/Y/G LEDs with a common anode (+) terminal
Off	Off	On	3-wire R/Y/G LEDs with a common cathode (-) terminal
Off	On	Off	3-wire bi-color R/G LED with a common anode (+) terminal
Off	On	On	3-wire bi-color R/G LED with a common cathode (-) terminal
On	Off	Off	2-wire bi-color R/G LED
On	Off	On	Reserved for future use
On	On	Off	Reserved for future use
On	On	On	Reserved for future use

Note: If a signal is configured as single-headed (SW1-4 for signal A, and SW1-5 for signal B), the LED outputs for the second head automatically become a 3-wire R/Y/G LED driver that mirrors the aspect of the head. This is useful for fascia repeaters, etc.

Table X-2: Signal Aspect Configuration for Single-Headed Signals
Switch Configuration		Aspect for Most Restricting Input
SW2-2 (A) / SW2-4 (B)	SW2-1 (A) / SW2-3 (B)	Stop	Advance Approach	Diverging / Approach	Approach	Clear
Off	Off	Red	Flashing Ylw	Yellow	Yellow	Green
Off	On	Red	Flashing Ylw	Green	Yellow	Green
On	Off	Red	Green	Yellow	Yellow	Green
On	On	Red	Green	Green	Yellow	Green

Table X-2: Signal Aspect Configuration for Dual-Headed Signals
Switch Configuration		Signal / Head	Aspect for Most Restricting Input
SW2-2 (A) / SW2-4 (B)	SW2-1 (A) / SW2-3 (B)		Stop	Advance Approach	Diverging / Approach	Approach	Clear
Off	Off	Upper	Red	Fl Ylw	Yellow	Yellow	Green
		Lower	Red	Red	Yellow	Red	Red
Off	On	Upper	Red	Fl Ylw	Yellow	Yellow	Green
		Lower	Red	Red	Green	Red	Red
On	Off	Upper	Red	Fl Ylw	Yellow	Yellow	Green
		Lower	Red	Red	Fl Green	Red	Red
On	On	Upper	Red	Green	Yellow	Yellow	Green
		Lower	Red	Red	Yellow	Red	Red

# Diagnostic Indicator Lights
LED Name / Color	Location	If Solid...	If Blinking...	If Off...
Red (D2)	Near “A Detector”	Track occupancy detected for A end block	Auxiliary occupancy A input is active	Occupancy not detected
Red (D3)	Near “B Detector”	Track occupancy detected for B end block	Auxiliary occupancy B input is active	Occupancy not detected
Red (IR / D8)	Near IR detector jack	Track occupancy detected by optical detector	Communications failure with IR sensor – check cable	Occupancy not detected
Yellow (ACT / D4)	Near IR detector jack	Board malfunction	Board is operating normally	Board malfunction
Green (PWR / D1)	Near IR detector jack	5V Power is on	Power is unstable or onboard regulator is overheating because of hardware failure or excessive input voltage	No power applied to PWR terminals or board has failed.
Green (3.3V / D10)	Near IR detector jack	3.3V Power is on	Power regulator failure due to overload, check IR sensor for shorts	No power to board or IR sensor cabling has a short
Green (12V / D9)	Near PWR connector	12V Power is on	Power regulator failure	No power to board or regulator failure

# Modular Signal System Bus
The Modular Signal System bus is constructed out of commodity network cables. An odd number of crossover elements – either crossover modules like this one or crossover Cat5 network cables – must exist between cascade elements. Typically a module with an MSS-CROSSOVER module will use the single crossover in the module itself, and use normal, “straight through” network cables to RJ45 female-female couplers at the end of the module. However, “crossover” type network cables can be used as long as they're used on both sides of the module, keeping a guaranteed odd number of crossovers between cascade modules.
Note: Only use “Cat5” or “Cat5e” type crossover cables. These only cross over two pair of the four within the cable. “Cat6” or “Cat7” crossover cables cross over all four pair, and will not work with the Modular Signal System.
For more details on the Modular Signal System, including the specification and other compatible products, see the MSS website:
http://modularsignalsystem.info/index.html
# Open Design
Iowa Scaled Engineering is committed to creating open designs that users are free to build, modify, adapt, improve, and share with others.
### Hardware
The design of the CKT-IRSENSE hardware is open source hardware, and is made available under the terms of the Creative Commons Attribution-Share Alike v3.0 license, a copy of which is available from: http://creativecommons.org/licenses/by-sa/3.0/
Design files can be found on the Iowa Scaled Engineering's Github site:
https://github.com/IowaScaledEngineering/mss-crossover
### Firmware
The official Iowa Scaled Engineering firmware for the MSS-CROSSOVER is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version. A copy of the GNU GPL can be found at: http://www.gnu.org/licenses/gpl.html
New firmware can be flashed into the MSS-CROSSOVER through J4. The six contacts are designed to mate with a Tag Connect TC2030-IDC-NL pogo-pin programming tail plugged into a standard AVR 6-pin ISCP programmer.

Iowa Scaled Engineering
http://www.iascaled.com/ support@iascaled.com